Intervalometer

A device to automatically trigger the shutter on a Nikon D80 camera using the MC-DC1 remote trigger cable.

Required:
1. The cable must continue to be usable as a handheld device
  1. Cable can be modified, but must still be usable independent of the intervalometer
  2. Modified cable required due to special connector on camera
  3. Cable can be extended
2. The trigger interval must be adjustable from 1 second to 10 minutes (600 seconds)
  1. May require multiple inputs to allow scaling (second, minute, hour)
3. Unit must have a display
  1. An LCD display will be used
  2. Display must have backlight for low light use
  3. Display must have adjustable contrast
4. Unit must display trigger interval
  1. Hours, minutes, seconds, total seconds
  2. Countdown to next trigger in seconds
5. Unit must display number of triggers that have occurred
6. Unit must be portable
  1. Small case
  2. Battery powered
  3. Somewhat weatherproof
7. User must be able to reset the unit
  1. Clear trigger count
  2. Reset interval to 0
8. User must be able to initiate triggering
9. User must be able to stop triggering